## Slide 1: U N I T I V
Network Security
Wireless Network Security
IEEE 802.11 Protocols C MAC Frame Structure
WAP Security • Monitor C Promiscuous Mode
Sniffing Wireless Packets
WLAN Authentication C Encryption
WEP • WPA • WPA2 • WPA3
Security Flaws • WLAN-Based Attacks
Countermeasures • WLAN Pen-Testing Tools
Bluetooth • ZigBee • RFID • NFC • Z-Wave • Cellular

## Slide 2: Unit IV — Course Map
01
IEEE 802.11 Protocols C MAC Frame
Structure
02
WAP Security • Monitor Mode •
Sniffing
03
WLAN Authentication C Encryption
(WEP/WPA/WPA2/WPA3)
04
WLAN Security Flaws C Attacks
05
Countermeasures C WLAN Pen-
Testing Tools
06
Other Wireless: Bluetooth • ZigBee •
RFID • NFC • Z-Wave

## Slide 3: IEEE 802.11 Protocols s MAC Frame Structure Standards evolution • Frame layout • Frame Control • ToDS/FromDS • Management subtypes • Beacon • Authentication exchange • RTS/CTS

## Slide 4: IEEE 802.11 — Standards Evolution
Standard | Year | Band | Max Speed | Security | Key Technology
802.11 (original) | 1997 | 2.4 GHz | 2 Mbps | WEP introduced | DSSS / FHSS
802.11a | 1999 | 5 GHz | 54 Mbps | WEP | OFDM
802.11b | 1999 | 2.4 GHz | 11 Mbps | WEP | DSSS
802.11g | 2003 | 2.4 GHz | 54 Mbps | WEP → WPA (2003) | OFDM
802.11n | 2009 | 2.4 / 5 GHz | 600 Mbps | WPA2 mandatory | MIMO · OFDM
802.11ac | 2013 | 5 GHz | 1.3 Gbps | WPA2 | MU-MIMO · 256-QAM
802.11ax (Wi-Fi 6) | 201G | 2.4 / 5 / 6 GHz | G.6 Gbps | WPA3 mandatory | OFDMA · 1024-QAM · BSS Color
APPLICATION
Security audit scenario: A building uses a legacy 802.11g AP. What security protocols is it limited to? What is
the minimum re-equipment required to support WPA3? Which frequency bands become available on
upgrade to 802.11ax?

## Slide 5: 802.11 MAC Frame — All Fields in Order
Frame Control
2 B
Duration
/ID
2 B
Address 1 (DA / RA)
6 B
Address 2 (SA / TA)
6 B
Address 3 (varies)
6 B
Seq Control
2 B
Addr 4 (WDS only)
6 B
Frame Body
0–7951 B
FCS
4 B
Frame Control (2B):
Most complex field — 16 bits defining frame type, subtype, and 9 control flags. See next slide for bit-level breakdown.
Duration/ID (2B):
NAV (Network Allocation Vector) in microseconds — tells other stations how long the medium will be occupied.
Address 1–3 (6B each):
IEEE 802 MAC addresses. Meaning (DA/SA/BSSID/RA/TA)
depends on ToDS and FromDS bits in Frame Control. See slide 7.
Sequence Control (2B):
Fragment number (4 bits) + Sequence number (12 bits). Used to filter duplicate frames and reassemble fragments.
Address 4 (6B):
Only present when ToDS=1 AND FromDS=1 (WDS bridge or mesh). Carries the Source Address in AP-to-AP transmissions.
Frame Body (variable):
Payload: 0 to 7,951 bytes for management frames; up to 2,346 bytes for data. Encrypted in WPA2/WPA3.
FCS (4B):
CRC-32 over the entire frame. Detects transmission errors. NOT
a security mechanism — WEP's CRC-32 is easily forged.
★ QoS Control (2B) present in 802.11e/WMM frames | HT Control (4B) in 802.11n/ac/ax | Maximum MAC header
= 36 bytes before payload

## Slide 6: Frame Control Field — 16-Bit Breakdown
0–1
Protocol Version
2–3
Type 00/01/10
4–7
Subtype (4 bits)
8
To DS
G
From DS
10
More Frag
11
Retry
12
Power Mgmt
13
More Data
14
Protected Frame
15
Order
/HTC+
Bit 0–1 — Protocol Version:
Always 00 for 802.11. Non-zero reserved.
Bit 2–3 — Type 00/01/10: Management=00, Control=01, Data=10 Bit 4–7 — Subtype (4 bits):
Identifies specific frame (e.g. 1000=Beacon, 1100=Deauth)
Bit 8 — To DS:
Frame destined for Distribution System
Bit G — From DS:
Frame originated from Distribution System
Bit 10 — More Frag:
More fragments follow this one
Bit 11 — Retry:
Retransmission of earlier frame
Bit 12 — Power Mgmt:
Station entering power-save mode after this frame
Bit 13 — More Data:
AP has more buffered frames for sleeping station
Bit 14 — Protected Frame:
WEP/WPA/WPA2/WPA3 encryption applied to Frame Body
Bit 15 — Order /HTC+:
Strict ordered processing; HT Control present in 802.11n+
ATTACK / FLAW
Bit 14 (Protected Frame) = 0 on ALL management frames in WPA2 — even Deauth frames are unencrypted. This is the
root cause of deauthentication attacks.

## Slide 7: ToDS / FromDS — Four Address Combinations
The four combinations of ToDS and FromDS determine the meaning of all four address fields. This is a standard examination question.
ToDS | FromD S | Network Topology / Scenario | Addr 1 | Addr 2 | Addr 3 | Addr 4
0 | 0 | IBSS (ad-hoc) — direct station to station, OR any Management/Control frame | DA | SA | BSSID | —
0 | 1 | Infrastructure — AP sending TO station (downlink) | DA | BSSID | SA | —
1 | 0 | Infrastructure — station sending TO AP (uplink) | BSSID | SA | DA | —
1 DA = Desti | 1 nation Addr | WDS bridge / Mesh — AP relaying to another AP ess SA = Source Address BSSID = AP MAC | RA RA = Receiver A | TA ddress TA = Tran | DA smitter Addres | SA s
WireshAPPLICATexerrka IONcise: capture frames and identify ToDS/FromDS values. Filter uplink traffic: wlan.fc.tods == 1 CC wlan.fc.fromds == 0. What are the address fields? This directly maps to the table above.

## Slide 8: Management Frames — Probe, Beacon s Authentication
0100 Probe Request
Sent by a client searching for known networks. Contains SSIDs from the device's Preferred Network List (PNL). Source MAC is the client's real hardware address (unless MAC randomisation is active on iOS/Android).
Reveals every SSID the device has ever connected to. Enables device tracking by MAC address. Basis of the Karma and MANA evil- twin attacks — rogue AP responds to all probes.
0101 Probe Response
Sent by AP in reply to a Probe Request matching its SSID. Contains full capability information including RSN IE. Transmitted even if the AP has SSID hiding enabled.
Exposes 'hidden' SSIDs. Any client probing for a hidden network by name causes the AP to respond with the SSID in plaintext. SSID hiding provides zero security.
1000 Beacon
Broadcast by AP every ~100ms (default 100 TU = 102.4ms). Contains: SSID, supported rates, DS Parameter Set (channel), Capability Info (Privacy bit), and critically — the RSN Information Element.
RSN IE declares cipher suites and AKM supported by AP. Spoofing a beacon with a modified RSN IE enables downgrade attacks — tricking clients into using weaker encryption.
1011 Authentication
Open System (2 frames): AP accepts all, no credential check. Shared Key (4 frames, WEP only): challenge-response using RC4 keystream. 802.11 authentication ≠ WPA2 authentication (that happens in EAPOL).
Shared Key paradox: challenge (plaintext) + response (ciphertext)
= 128 bytes of exposed RC4 keystream. Attacker forges authentication without knowing the key. Open System is SAFER.
Notes: RSN: Robust Security Network

## Slide 9: Management Frames — Deauth, Association s RTS/CTS
1100 Deauthentication Most commonly spoofed 802.11 frame
Contains a 16-bit Reason Code (unspecified=1, leaving IBSS=3,
inactivity=4, AP overloaded=5). Frame carries NO cryptographic authentication in WPA2 — any station can spoof the AP's MAC address and send a deauth to any client.
ATTACK:
aireplay-ng -0 5 -a [AP MAC] -c [Client MAC] wlan0mon
→ Client disconnects → re-
authenticates → attacker captures
fresh EAPOL handshake
FIX: 802.11w Protected Management Frames (PMF) adds MIC to
Deauth/Disassoc. Mandatory in WPA3.
1010 Disassociation
Also spoofable without 802.11w. Used for targeted DoS. Client must re-associate (not re-authenticate) — slightly less disruptive than Deauth but still weaponisable.
0000/0001 Association Req/Response
Client's RSN IE must exactly match AP's Beacon RSN IE — mismatch = rejection. AP assigns Association ID (AID). Triggers the WPA2 4-way handshake immediately after.
1101 Action Frames
Spectrum management, Block ACK setup, Radio Measurement, 802.11w PMF negotiation, Fine Timing Measurement (FTM) for indoor positioning.
RTS/CTS — Control Frames — Hidden Node Problem Solution
Station A and C cannot hear each other but both hear AP B. A sends RTS → B replies CTS (broadcast) → All stations set NAV timer and defer → A transmits safely. Forged RTS/CTS frames set NAV of all stations to maximum duration → virtual carrier-sense DoS — legitimate traffic completely blocked.

## Slide 10: Beacon Frame — Information Elements
The Beacon is the most security-relevant management frame. Broadcast every ~100ms. Every client in range reads it.
Timestamp (8 B)
AP clock value. Clients synchronise their TSF timer to this. Used in power management and channel timing.
Beacon Interval (2 B)
Default 100 TU (Time Units) = 102.4 milliseconds. The interval at which the AP broadcasts beacons.
Capability Information (2 B)
Privacy bit = 1 means encryption is active. ESS/IBSS mode flag. Short preamble, PBCC, channel agility flags.
SSID IE
Network name. Set to zero-length for 'hidden' networks —
but SSID is still revealed in Probe Responses and Association Requests.
Supported Rates IE
Data rates the AP supports and requires. Used in capability negotiation with associating clients.
DS Parameter Set (3 B)
Current operating channel number. Used by clients to determine which channel to listen on.
RSN Information Element
Declares WPA2/WPA3 cipher suites (CCMP, GCMP), AKM
suites (PSK, 802.1X, SAE), and PMF capability. Spoofing this
element in a forged beacon enables downgrade attacks.
WPS IE (Vendor Specific)
Signals Wi-Fi Protected Setup availability. Presence of this
IE is detectable — indicates potential WPS PIN attack vector.
APPLICATION
Wireshark filter for RSN IE: wlan.rsn.ie | Check AKM suite for PSK (02) vs 802.1X (01) vs SAE (08) | PMF required = bit 7 of RSN Capabilities
Notes: RSN: Robust Security Network

## Slide 11
WAP Security • Modes • Sniffing
Rogue AP • Evil Twin • Karma/MANA • Promiscuous vs Monitor Mode • Wireless Packet Capture

## Slide 12: WAP — Inherent Security Issues
Rogue / Unauthorised AP
An employee installs a personal AP behind the corporate firewall without informing the network administrator. The device has no enterprise security configuration and sits on the internal LAN. The corporate firewall offers no protection against an attacker who associates with the rogue AP.
A penetration tester discovers an unauthorised TP-Link AP in a conference room. It is bridging to the corporate VLAN. What are the immediate risks, and what forensic evidence does the AP contain?
Evil Twin Attack
Attacker clones the target SSID with an equal or stronger
signal. Client devices automatically select the strongest signal
— no user action required. Attacker gains full man-in-the- middle position: captures plaintext credentials, injects DNS
responses, strips HTTPS with sslstrip.
'CafeWifi_Free' matching the legitimate SSID. A customer o
Coffee shop scenario: attacker sets up a hotspot named
pens
online banking. What data is at risk and what tools does the attacker use?
PNL Exploitation — Karma / MANA
Devices continuously broadcast Probe Requests for every SSID in their Preferred Network List. A Karma-enabled rogue AP responds to all probes — the device auto-connects silently.
MANA extends this to WPA2-Enterprise: rogue RADIUS server harvests MSCHAPv2 credential hashes.
A corporate laptop has 'HotelNet' and 'AirportWiFi' in its PNL. An attacker at the airport runs a Karma AP. Describe the attack chain and what data is captured.
SSID Hiding — A False Sense of Security
Setting SSID to zero-length in Beacon only removes the name from passive discovery. The SSID is fully revealed in: (1) Probe Responses when any client queries it, (2) Association Request frames in plaintext. Airodump-ng displays hidden SSIDs within seconds of any client activity.
An IT manager hides the SSID of the management VLAN access point and claims it is now secure. How would you demonstrate this is ineffective using only Kali Linux and a wireless adapter?

## Slide 13: Promiscuous Mode vs Monitor Mode (RFMON)
Promiscuous Mode
NIC must first authenticate and associate with an AP
SSID filter remains active — only the associated network is visible
Receives all frames on the associated network (not
just its own)
802.11 MAC header is stripped — frames delivered
Ethernet-style to OS
Cannot see management frames of other networks
Works on both wired and wireless networks
Useful for analysing your own network traffic
Set in Linux: ip link set wlan0 promisc on (still
requires AP association)
Monitor Mode (RFMON)
No AP association required — purely passive RF receiver
SSID filter disabled — ALL 802.11 frames on selected channel are captured
Captures frames from ALL SSIDs simultaneously
Full 802.11 MAC header preserved — forensically
complete frames
Captures: management frames, EAPOL handshakes, beacon/probe data
Can be tuned to a specific channel or set to channel-hop
Required for wireless forensics and penetration testing
Enable in Linux: airmon-ng start wlan0 → creates
wlan0mon interface
FORENSIC RELEVANCE: Monitor mode is the correct and only acceptable mode for wireless evidence collection in a forensic investigation. It captures the complete 802.11 frame including MAC headers (stripped in promiscuous mode), enabling capture of EAPOL 4-way handshakes, deauth floods, probe request histories (device presence at location), beacon RSN IE anomalies, and management frame injection attacks. airodump-ng captures to .pcapng for Wireshark analysis.

## Slide 14: Sniffing Wireless Packets — What Is Visible
The 802.11 medium is shared and broadcast. Any NIC in monitor mode within RF range captures every frame on the active channel — no decryption key required.
Visible WITHOUT any key | Visible WITH the encryption key | Wireshark Useful Filters
All SSID names from Beacon and Probe Response frames Client MAC addresses from Probe Requests (unless randomised) Client's Preferred Network List — every SSID probed AP capabilities including RSN IE (cipher suites, PMF status) EAPOL 4-way handshake frames (for offline attack) | Complete decrypted data payloads (HTTP, DNS, SMTP traffic) DHCP exchanges — reveals internal IP addressing scheme DNS queries — reveals websites/services being accessed Unencrypted application-layer credentials (HTTP Basic Auth, FTP) Internal network topology from ARP and routing traffic | eapol — capture 4-way handshake messages wlan.fc.type_subtype == 0x08 — Beacon frames only wlan.fc.type_subtype == 0x04 — Probe Request frames wlan.fc.type_subtype == 0x0c — Deauthentication frames wlan.addr == [MAC] — filter specific device
IV values in WEP-protected frames |  | 
All management frame exchanges — auth, assoc, deauth sequences Frame sizes and timing — traffic analysis even when encrypted |  | 
APPLICATION: Investigator at a crime scene turns on monitor mode and runs airodump-ng. Within 5 minutes they have: (1) list of all APs in range with SSIDs and channels, (2) list of client devices with MAC addresses, (3) which SSIDs each client device has previously connected to. This intelligence is collected passively with zero interaction with any network.

## Slide 15
WLAN Authentication s Encryption
WEP • WPA • WPA2 • WPA3 • 4-Way Handshake • KRACK • PMKID • SAE

## Slide 16: WLAN Authentication — Part 1: Open System s Shared Key
These are the two original 802.11 authentication methods. Both are pre-WPA. Understanding their flaws is essential — Shared Key is directly examined.
Open System Authentication
2-frame exchange — no credentials whatsoever
① STA → AP: Auth Request (Algorithm=0,
Sequence=1)
② AP → STA: Auth Response (Algorithm=0,
Sequence=2, Status=0 ✓)
AP accepts ALL stations unconditionally — no key, no password, no identity check. Zero security on its own. Legitimately used behind captive portals where application-layer authentication (e.g. voucher, certificate, user login) is applied after association.
→ Use only for guest portals with application- layer control. Never for corporate access.
Shared Key Authentication (WEP only — 4 frames)
Auth Request Challenge Text
(Algorithm=1, Seq=1) (128-byte PLAINTEXT)
Challenge Response (128 bytes RC4-
① STA → AP:
② AP → STA:
③ STA → AP:
encrypted)
④ AP → STA:
Success / Failure
CRITICAL PARADOX
Frame ② = plaintext challenge
Frame ③ = RC4(same plaintext)
② XOR ③ = 128-byte RC4 keystream exposed Attacker forges future Auth Requests WITHOUT knowing the WEP key.
Open System is cryptographically SAFER.

## Slide 17: WLAN Authentication — Part 2: PSK, 802.1X / EAP s SAE
PSK — Pre-Shared Key (WPA/WPA2-Personal)
Passphrase (8–63 ASCII chars) converted to a 256-
bit PMK via PBKDF2-SHA1 with 4,096 iterations. PMK drives the 4-Way Handshake to derive per- session traffic keys.
PMK = PBKDF2-SHA1( passphrase, SSID,
4096, 32B )
Handshake captured passively → Hashcat offline crack.
→ Home/SOHO only with 20+ char random passphrase.
NOT enterprise — one leak exposes key for ALL users.
802.1X / EAP — Enterprise (WPA2/WPA3)
Port-based access control. AP (authenticator)
relays EAP between client (supplicant) and RADIUS server. PMK derived per-session from RADIUS —
never fromMautsuhalacreerdtipficaastsepsh(craliesnet.+ server). Strongest — no
EAP-TLS: password to crack.
PEAP: Server cert only. MSCHAPv2 inside TLS. Vulnerable if cert
EAP-TTLS: not validated.
Like PEAP but supports multiple inner methods
EAP-FAST:(PAP/CHAP/MSCHAPv2).
Cisco PAC-based. No certificates needed. Simpler dply.
SAE — Simultaneous Authentication of Equals (WPA3-
Personal) | Dragonfly Key Exchange
Zero-knowledge key exchange — neither side sends the passphrase, a hash of it, or any derivable value over the air. Each SAE exchange produces a unique, fresh PMK. Every authentication attempt requires active real-time interaction with the AP — offline dictionary attacks are mathematically impossible, as the attacker cannot accumulate material to analyse independently.
Current Best Practice
Eliminates offline PSK attacks entirely. Passwords can be shorter than WPA2- PSK and still be secure.
Forward Secrecy: per-session PMK — past traffic cannot be decrypted even if passphrase later compromised.

## Slide 18: WEP — Wired Equivalent Privacy (1GG7 · Deprecated 2004)
Step 1:
Step 2:
Step 3:
ICV = CRC-32 (Plaintext Data) —
append ICV to data
RC4 key = IV (3 bytes) || WEP
Key (40 or 104 bits)
Ciphertext = (Data || ICV) XOR RC4 (IV || Key)
TX Frame:
[MAC Header] [Ciphertext]
[IV 3B | KeyID 1B] [FCS 4B]
THE FLAW:
IV transmitted in PLAINTEXT —
attacker sees every key reuse
Encryption Mechanism Four Critical Weaknesses
IV Collision — FMS/PTW Attack
Only 2²⁴ = 16.7 million IVs. Busy networks reuse IVs within
hours. FMS attack (2001) uses statistical analysis of weak IVs. PTW attack (2007) needs just 5,000 IVs. Aircrack-ng with
packet injection: key recovered in < 60 seconds.
CRC-32 Integrity Flaw
CRC-32 is a linear function — not a Message Authentication
Code. Attacker flips bits in the ciphertext and recalculates a valid ICV without knowing the key. Malicious payload
injection succeeds.
Shared Key Auth Paradox
Challenge text (plaintext) XOR challenge response
(ciphertext) = 128 bytes of RC4 keystream. Attacker forges future authentication frames without ever knowing the WEP
key.
No Key Management
All users share one static key forever. No per-session, per- user, or per-packet keys. Key revocation requires manual
reconfiguration of every single device on the network.
VERDICT: WEP provides no meaningful confidentiality, integrity, or authentication. Any WEP-protected network must be treated as an open network. Aircrack-ng breaks WEP in minutes. Migrate to WPA2-Enterprise as the absolute minimum.

## Slide 19: WPA (2003) — TKIP, Personal, Enterprise s Beck-Tews
WPA was an emergency interim standard released in 2003 while IEEE 802.11i (WPA2) was finalised. Designed to run as a firmware update on existing WEP hardware — same radios, new protocol.
TKIP — Temporal Key Integrity Protocol
Per-packet key mixing: each frame gets a unique RC4 key derived from the base key, Transmitter MAC, and a 48-bit IV (eliminating WEP's IV collision). Michael MIC replaces broken CRC-32. Designed to run on existing WEP hardware via firmware update — same RC4 chip,
new key schedule.
Firmware upgrade from WEP — same hardware
WPA-Personal (WPA-PSK)
Passphrase 8–63 chars. PMK = PBKDF2- SHA1(passphrase, SSID, 4096, 32B). The 4-Way Handshake uses PMK to derive per-session TK. The handshake is capturable passively and the PMK brute- forceable offline with Hashcat. PMKID attack (2018)
doesn't even need the handshake.
Offline dictionary attack — capture + crack
WPA-Enterprise (802.1X / RADIUS)
  X port-based access control. AP relays EAP between client and RADIUS server. PMK derived per- session from RADIUS — never a shared passphrase. One compromised credential does not affect any other user. No handshake to capture for offline attack.
    No shared passphrase — no offline attack
Beck-Tews Attack (2008) — TKIP Broken
Demonstrated partial decryption and re-injection of short WPA-TKIP frames (e.g. ARP requests) using a chopchop- based technique. Confirms TKIP is cryptographically broken. WPA-TKIP is deprecated — it must not be used.
AES-CCMP (WPA2) is the minimum acceptable cipher.
TKIP deprecated — use AES-CCMP minimum

## Slide 20: The 4-Way Handshake — PTK Derivation
The 4-Way Handshake establishes per-session traffic keys without transmitting the PMK. Both AP and STA prove they hold the same PMK — without ever revealing it.
MSG 1
AP → STA
ANonce (AP's fresh 32-
byte random nonce)
AP generates a new random nonce (ANonce). STA receives it and — combined with its own SNonce (generated next) — now has all inputs needed to compute the PTK.
MSG 2
RSN IE +
STA → AP
SNonce +
MIC
STA generates SNonce, computes PTK using PMK+ANonce+SNonce+MACs, then sends SNonce + its cipher suite preferences (RSN IE) + a MIC to prove PMK knowledge. AP computes PTK, verifies MIC.
MSG 3
AP sends the Group Temporal Key (for broadcast/multicast) encrypted with KEK from the PTK. MIC proves integrity. STA installs GTK and TK. KRACK exploits retransmission of this message.
MSG 4
AP → STA
GTK (encrypted with KEK)
+ MIC
STA → AP
MIC only
(acknowledgement)
STA confirms GTK installation. Handshake complete. Both sides begin encrypting data with TK. GTK is refreshed when a client disconnects or at periodic intervals.
PTK = PRF-384 ( PMK || ANonce || SNonce || AP-MAC || STA-MAC )
Splits into: KCK (16B — MIC key for handshake messages) | KEK (16B — encrypts GTK in MSG 3) | TK (16–32B —

## Slide 21: WPA2 — AES-CCMP s KRACK (Key Reinstallation Attack)
WPA2 (IEEE 802.11i, 2004) replaces RC4/TKIP with AES-CCMP — a fundamentally stronger cipher. Mandatory
for Wi-Fi certification since 200c.
Counter Mode (CTR) —
Confidentiality
AES-128 in Counter Mode. Each 128-bit
block is XOR'd with AES-encrypted (nonce + counter). Counter increment prevents any two blocks sharing a
keystream segment. Completely
CBC-MAC Protocol — Integrity s Auth
Cipher Block Chaining MAC provides
cryptographic integrity AND data-origin authenticity in the same pass as encryption. 8-byte MIC appended to
ciphertext. Replaces WEP's broken CRC-
48-bit Packet Number (PN)
Monotonically increasing 48-bit counter per key. Prevents replay attacks.
Incorporated into the nonce for each frame. Nonce reuse with AES-CTR is
catastrophic — KRACK forces exactly
Mechanism:
Attacker retransmits MSG 3 of the 4-way handshake. WPA2 spec requires the STA to reinstall the TK and RESET the 48-bit PN counter to zero on receiving a retransmitted MSG 3. PN reset = nonce reuse = AES-CTR keystream reuse = plaintext recovery.
Impact:
Affects ALL WPA2 devices ever manufactured — a protocol design flaw, not a software bug. Both CCMP and TKIP affected. Within Wi-Fi range, attacker decrypts victim traffic, injects or forges frames, and replays old packets.
Mitigation:
OS patch prevents nonce reset on retransmit. WPA3 SAE handshake is immune by design. Enable 802.11w PMF. Unpatched IoT — cameras, thermostats, smart appliances — remain permanently vulnerable.
Application: Which devices on your network have never received the KRACK patch? IoT manufacturers typically release one firmware update in year 1 — then abandon the device. The average home has 10+ permanently unpatched WPA2 devices.
replaces WEP/TKIP's RC4. 32 and WPA's Michael MIC. this.
KRACK — Key Reinstallation Attack (Mathy Vanhoef, 2017 | CVE-2017-13077 to 13088)

## Slide 22: WPA2 — PMKID Attack s Personal vs Enterprise
PMKID Attack — Jens Steube (Hashcat author), 2018
PMKID = HMAC-SHA1-128 ( PMK , "PMK Name" || AP-MAC || STA-MAC )
Derivable from a SINGLE EAPOL frame (the association response) — no complete 4-way handshake needed
No client deauthentication required — the attack is completely passive
Collected from a single beacon or association response from any access point
Submit directly to Hashcat: hcxpcapngtool capture.pcapng → hashcat -m 22000
hash.hc22000 wordlist.txt
WPA2-Personal vs WPA2-Enterprise — Choosing the Right Mode:
WPA2-Personal (PSK)
Single passphrase shared by ALL users
PMK = PBKDF2-SHA1(passphrase, SSID, 4096, 32B)
EAPOL handshake capturable → Hashcat offline
PMKID capturable from a single EAPOL frame
One compromised user = all users at risk
Home/SOHO only. Passphrase: 20+ random chars.
WPA2-Enterprise (802.1X / EAP)
Unique credential per user — cert or username+pw
PMK derived per-session from RADIUS — never shared
No handshake or PMKID exposes the PMK derivation
Offline dictionary attack vector does not exist
One compromised credential affects only that user
All enterprise WLANs. EAP-TLS + mutual certs = gold standard.

## Slide 23: WPA3 — SAE • OWE • DPP • Forward Secrecy • 802.11w
1.48
Zero-knowledge key exchange replaces the PSK 4-way handshake. Neither side sends the password or any derivation of it over the air. Each SAE exchange produces a unique PMK — there is no handshake to capture. Every authentication guess requires active interaction with the AP (online-only brute force), making automated offline attacks impossible regardless of passphrase weakness.
1.35
Each session derives a unique PMK via SAE. Compromise
of the long-term network passphrase at a later date does NOT allow decryption of previously captured session traffic. This is critical for organisations that may face retrospective decryption attacks from adversaries storing encrypted
captures.
1.35
Encrypts open (no-password) network sessions using Diffie-Hellman key exchange. No authentication — but
provides confidentiality against passive sniffing on café and
airport Wi-Fi networks. Transparent to users.
1.34
Replaces WPS and its split-PIN design flaw. Uses QR code or NFC tap to securely provision IoT devices. The configurator (e.g. smartphone) provisions network credentials to the enrollee device without exposing the passphrase. No Reaver-style PIN brute-force possible.
1.34
GCMP-256 encryption + HMAC-SHA-384 key derivation + BIP-GMAC-256 for management frame protection. Aligned to the CNSA (Commercial National Security Algorithm) suite for government and classified environments.

## Slide 24: WEP • WPA • WPA2 • WPA3 — Side-by-Side
Feature | WEP (1GG7) | WPA (2003) | WPA2 (2004) | WPA3 (2018)
Cipher | RC4 (stream) | RC4 + TKIP | AES-CCMP (block) | AES-CCMP / GCMP- 256
Integrity | CRC-32 (flawed) | Michael MIC | CBC-MAC (strong) | CBC-MAC / GMAC
Key size | 40 or 104 bits | 256-bit PMK | 128-bit TK | 128–256 bit TK
IV size | 24 bits (reused in hours) | 48 bits (no reuse) | 48-bit PN | 48-bit PN
Authentication | Open / Shared Key | PSK or 802.1X | PSK or 802.1X | SAE or 802.1X
Forward Secrecy | ✗ | ✗ | ✗ | (per-session PMK)
Offline attack | Yes (FMS/PTW, minutes) | Yes (handshake) | Yes (KRACK/PMKID) | No (online-only)
Mgmt Frame Prot. | None | None | Optional (PMF) | Mandatory (PMF)
Status | BROKEN — never use | Deprecated | Minimum standard | Current best practice
APPLICATION An organisation's WLAN audit reveals WPA2-Personal with the passphrase 'CompanyName2024'. Which specific attacks apply? What is the recommended remediation path — and in what order should controls be implemented? |  |  |  | 

## Slide 25
WLAN Security Flaws s Attacks
Auth flaws • Deauth flood • Evil Twin • WPS PIN • PMKID • FragAttacks • RF Jamming • MitM

## Slide 26: WLAN Authentication Security Flaws
WEP Shared Key — Keystream Exposure
Frames 2 (plaintext challenge) XOR Frame 3 (RC4 ciphertext) = 128 bytes of RC4 keystream. An attacker with a packet capture can forge future authentication requests without ever knowing the WEP key. Open System authentication is cryptographically safer than WEP Shared Key authentication.
With Wireshark, filter for: wlan.fc.type_subtype == 0x0b (Authentication frames). Capture a Shared Key exchange. Identify frames 1–4. Demonstrate the keystream exposure.
WPA/WPA2 PSK — Offline Dictionary Attack
The complete attack chain: (1) airodump-ng to identify target AP and connected clients. (2) aireplay-ng -0 deauth to force client re-authentication. (3) airodump-ng captures the EAPOL 4-way handshake. (4) aircrack-ng or Hashcat -m 22000 runs offline dictionary/mask attack. (5) GPU benchmark: ~1.5M PMKs/second on RTX 3080. A passphrase in rockyou.txt is cracked in seconds.
Estimate crack time: passphrase 'wifi2024' vs
'9xT#mK7!pQ3vL8@n' at 1.5M PMKs/sec. Which is in rockyou.txt?
Why does passphrase length matter more than complexity for
WPA2-PSK?
KRACK — Key Reinstallation (2017)
MSG 3 replay forces PN reset to zero. AES-CTR nonce reuse = keystream reuse = decryption of all subsequent traffic. Affects every WPA2 device ever manufactured. The attack does NOT require knowing the passphrase.
Which devices in your home/office are likely still unpatched?
Identify IoT device categories (security cameras, smart TVs,
printers) that typically never receive firmware updates. What is the residual risk?
PMKID Attack (2018) s FragAttacks (2021)
PMKID: HMAC-SHA1-128(PMK, 'PMK Name'||AP-MAC||STA-
MAC) — derivable from a single EAPOL frame without any client. FragAttacks CVE-2020-24588: A-MSDU injection allows injecting plaintext frames into an encrypted WPA2 session.
Design flaw present in 802.11 since 1997.
FragAttacks demonstration: attacker on same network can inject a forged DNS response into an encrypted WPA2 session, redirecting the victim to an attacker-controlled server — even through WPA2 encryption.

## Slide 27: WLAN-Based Attacks — Mechanics s Commands
Deauthentication Flood
aireplay-ng -0 0 -a [AP] wlan0mon
Continuous spoofed Deauth frames to all clients. Forces constant re- authentication — AP is rendered unusable. Deauth of a specific client forces EAPOL handshake for capture.
Fixed by 802.11w PMF.
Rogue AP / Evil Twin
hostapd + dnsmasq + sslstrip
Clone SSID with stronger signal. Client auto-associates. sslstrip downgrades HTTPS to HTTP. Ettercap or Bettercap intercepts all traffic. Hostapd-WPE harvests EAP credentials from Enterprise clients.
WPS PIN Brute-Force
wash -i wlan0mon | reaver -i
wlan0mon -b [AP] -vv
WPS 8-digit PIN split into two independent 4-digit halves. Max 10,000 + 1,000 = 11,000 attempts (not 10⁸). wash identifies WPS-enabled APs. Reaver automates. PIN recovery gives PSK directly.
RF Jamming (DoS)
No 802.11 frames — SDR required
Broadband 2.4 / 5 GHz interference.
Selective targeting of one channel. No
802.11 frames transmitted — traditional WIDS may not detect it. Requires
spectrum analyser for attribution.
Karma / MANA Attack
hostapd-mana mana.conf
Rogue AP responds to all Probe Requests matching client PNL. Device auto- connects. MANA adds EAP harvesting via rogue RADIUS for Enterprise networks.
Completely automated credential
harvesting.
MitM Follow-on Attacks
arpspoof / Bettercap / dnsspoof
After rogue AP association: ARP poisoning intercepts LAN traffic. DHCP spoofing controls DNS and gateway. DNS hijacking redirects to attacker sites. SSL stripping downgrades HTTPS. Credential harvesting without any encryption bypass.

## Slide 28
Countermeasures
s WLAN Pen-Testing Tools
WPA3 • 802.11w • EAP-TLS • WIDS/WIPS • Aircrack-ng • Kismet • Wireshark • Hashcat •
Reaver

## Slide 29: WLAN Countermeasures — Protocol s Authentication Controls
PROTOCOL SELECTION
Deploy WPA3 for all new access points — SAE eliminates offline
attack
Minimum WPA2-Enterprise (802.1X/RADIUS) for existing
infrastructure
Disable WEP, TKIP, and WPA entirely — no legacy protocol
exceptions
Disable WPS on ALL access points — no exceptions. WPS =
known design flaw
Enable 802.11w Protected Management Frames — mandatory on WPA3, enforce on WPA2
AUTHENTICATION ARCHITECTURE
WPA2/3-Enterprise: 802.1X with RADIUS server (FreeRADIUS or
commercial)
EAP-TLS: mutual certificate authentication — strongest EAP method available
PEAP: server certificate MUST be validated by client — prevents
rogue RADIUS harvest
Avoid LEAP and EAP-MD5 — both are deprecated and dictionary-
attackable
Certificate-based auth: each user has unique credential; one
compromise ≠ all compromised
NETWORK SEGMENTATION
WLAN in a separate VLAN/DMZ — no direct access to wired corporate LAN
Guest WLAN: fully isolated segment with internet-only
access and captive portal
IoT WLAN: dedicated SSID, no access to corporate
r▸esRoFurscitees,seugrvreesy:smfilateprsiniggnal coverage, identify leakage outside building perimeter
MAC filtering: supplementary control only — MAC addresses are trivially spoofed
DETECTION s MONITORING
WIDS/WIPS: detect rogue APs, deauth floods, probe storms, beacon anomalies
RF-based detection: RSSI triangulation to physically locate rogue APs
Correlate AP association logs + DHCP leases to identify
unknown clients
Monitor for deauth frame spikes — WIDS threshold alert
within seconds
Periodic wireless penetration tests — Aircrack-ng, Kismet,
Wifite, Hashcat

## Slide 30: WLAN Pen-Testing Tools — Part 1
Aircrack-ng Suite
Industry-standard Kali Linux wireless audit toolkit. Four key tools:
airmon-ng (enable monitor mode), airodump-ng (passive capture on specified channel and BSSID), aireplay-ng (packet injection and deauthentication), aircrack-ng (PTW attack for WEP, dictionary attack
for WPA/WPA2).
wlan0mon
airmon-ng start wlan0
airodump-ng -c 6 --bssid [AP] -w cap
wlan0mon
aireplay-ng -0 5 -a [AP] -c [Client]
aircrack-ng -w
/usr/share/wordlists/rockyou.txt cap.cap
Kismet
Passive wireless scanner operating in monitor mode. Detects SSIDs
(including 'hidden' ones via probe responses), maps client devices, identifies BSSIDs, channels, and encryption types. GPS logging for RF mapping and site survey. Acts as a WIDS — detects deauth floods and
rogue APs. Outputs raw PCAP for Wireshark analysis.
kismet -c wlan0mon
kismet --override wardrive

## Slide 31: WLAN Pen-Testing Tools — Part 2
Wireshark / tshark
Protocol analyser for deep 802.11 frame dissection. Dissects
management, control, and data frame structures. Visualises the complete EAPOL 4-way handshake with each message labelled. Decrypts WEP/WPA2 traffic when encryption key is known. Beacon
RSN IE inspection identifies cipher suites and PMF capability.
eapol
wlan.fc.type_subtype == 0x0c wlan.rsn.ie
wlan.ssid == 'TargetNet'
Hashcat
GPU-accelerated offline password cracking. hcxtools converts .pcapng
captures to Hashcat format (.hc22000). Mode 22000 handles both WPA-PBKDF2 and PMKID. Attack modes: wordlist, wordlist+rules, mask (pattern-based), combinator. Benchmark: RTX 3080 achieves
~1.5 million PMKs/second. A passphrase in rockyou.txt is cracked in seconds.
hcxpcapngtool -o hash.hc22000 capture.pcapng
hashcat -m 22000 hash.hc22000 wordlist.txt hashcat -m 22000 hash.hc22000 -a 3
?u?l?l?l?d?d?d?d

## Slide 32: WLAN Pen-Testing Tools — Part 3
Reaver / Bully
WPS PIN brute-force tool exploiting a fundamental design flaw: the 8-
digit PIN is verified in two independent halves (first 4 digits, then last 4
+ checksum). Maximum 10,000 + 1,000 = 11,000 attempts rather than
10⁸. wash scans for WPS-enabled APs and reports lock status. Successfully recovering the PIN provides the PSK passphrase directly.
COUNTERMEASURE: Disable WPS entirely on all APs.
wash -i wlan0mon (detect WPS-enabled APs)
reaver -i wlan0mon -b [AP MAC] -vv bully wlan0mon -b [AP MAC] -d
Hostapd-WPE
Rogue WPA2-Enterprise AP tool for EAP credential harvesting. Sets up a convincing WPA2-Enterprise access point with a self-signed certificate. Clients that connect without validating the server certificate
submit MSCHAPv2 challenge-response hashes. asleap or Hashcat mode 5500 cracks the NTLMv2 hash offline. Exploits the most common
PEAP misconfiguration: missing server certificate validation.
hostapd-wpe /etc/hostapd-wpe/hostapd- wpe.conf
asleap -C [challenge] -R [response] -W wordlist.txt
APPLICATION
Pen-test methodology: Passive recon (Kismet) → Target selection → Deauth + EAPOL capture (Aircrack-ng) → Offline crack (Hashcat) → Report with PSK and remediation. For Enterprise: Rogue AP (Hostapd-WPE) → Harvest MSCHAPv2 → Crack with asleap.

## Slide 33
Other Wireless Protocols
Bluetooth • BLE • ZigBee • Z-Wave • RFID • NFC • WiMAX • Cellular • IrDA

## Slide 34: Bluetooth — Versions, Security s Attacks
Version Timeline
Version | Year | Key Feature / Security Note
1.0 / 1.1 | 1999 | Fixed device address in every frame → trivial device tracking
2.1 + EDR | 2007 | Secure Simple Pairing (SSP) — replaces vulnerable PIN-based pairing
4.0 | 2010 | BLE (Low Energy) introduced. Dual-mode. Low-power IoT focus.
4.2 | 2014 | AES-CCM for BLE (LESC). Resolvable Private Addresses for anti-tracking. IPv6.
5.0 | 2016 | 2× speed (2 Mbps), 4× range, 8× broadcast capacity. AoA/AoD direction finding.
5.2 | 2020 | LE Audio, EATT, LC3 codec. Isochronous channels for hearing aids.
5.4 | 2023 | PAwR for IoT mesh. Improved duty cycle management.

## Slide 35: Bluetooth — Versions, Security s Attacks
Key Vulnerabilities
BlueBorne (2017)
8 zero-day vulnerabilities across Android, iOS, Windows, Linux. Airborne RCE — no pairing, no discoverable state, no user interaction required. Spreads device-to-device silently. 5.3 billion devices affected at disclosure.
KNOB Attack (201G)
Key Negotiation Of Bluetooth: forces session key entropy down to 1 byte (1 bit). Brute-forced in milliseconds on any hardware. Affects ALL Classic Bluetooth versions regardless of pairing mode.
BIAS Attack (2020)
Bluetooth Impersonation AttackS: exploits Secure Connections role switching to authenticate as a previously paired device without possessing the link key.
BLESA (2020)
BLE Spoofing Attack on reconnection procedure. Bypasses device re-authentication on BLE reconnect. Affects iOS,
Android, and Linux BLE stacks.
Bluesnarfing / Bluebugging
Medical device scenario: An insulin pump uses Bluetooth 4.0 BLE. Identify the applicable vulnerabilities (BLESA reconnect spoof, BLE eavesdropping, unencrypted GATT characteristics). What are the life-safety implications? What controls can a hospital implement?

## Slide 36: ZigBee • Z-Wave • RFID • NFC — Features s Vulnerabilities
ZigBee (IEEE 802.15.4)
2.4 GHz mesh networking. AES-128 encryption. 250 kbps. Up to 65,000 nodes per network. Designed for smart home automation, industrial SCADA, and building management.
Network key transmitted in PLAINTEXT during device join unless specifically protected. Default key 'ZigBeeAlliance01' widely known. 32-bit frame counter → replay attack vulnerability. KillerBee toolkit (Python) supports capture, injection, replay, and key extraction.
Smart building: KillerBee intercepts the join handshake when a new Zigbee sensor is added to the network. Attacker captures the network key and can now inject commands to any device on the network — including opening smart door locks or triggering fire suppression systems.
Z-Wave (ITU-T G.GG5G)
Sub-GHz bands (868 MHz EU / 908 MHz US). Avoids 2.4 GHz congestion. 30–100m range. Maximum 232 nodes. Widely used in smart locks, thermostats, and access control. S2 framework (2017) uses ECDH for key exchange.
S0 (pre-2017 devices): network key XOR'd with 0x00×16
— mathematically equivalent to plaintext transmission. S0→S2 downgrade attack forces inclusion in vulnerable S0 mode. SDR (Software Defined Radio) captures sub-GHz RF
traffic.
A corporate building uses Z-Wave smart locks on server room doors. Verify device firmware dates. Any lock using S0 security must be replaced — SDR + Gqrx + GNU Radio can capture the plaintext key during lock pairing.

## Slide 37: ZigBee • Z-Wave • RFID • NFC — Features s Vulnerabilities
RFID
LF (125 kHz): animal tags, HID access cards — NO encryption, NO challenge-response. HF (13.56 MHz, ISO 14443): contactless smart cards with optional AES. UHF (860–960 MHz): EPC Gen2 supply chain — 12m range, no strong authentication.
LF cards (EM4100, HID Prox) trivially cloned with Proxmark3 or Flipper Zero in seconds. Relay attack: two NFC/RFID devices proxy a card transaction over any distance — contactless payment fraud, access card cloning without physical possession. No encryption in LF, no PKI anywhere.
Physical security test: use a Proxmark3 to clone an HID Prox access card from an employee in the lift (elevator) within 15cm. Use the clone to access restricted areas.
Demonstrate why 'card = identity' is a flawed security
model.
NFC (ISO 180G2 / NFC Forum)
13.56 MHz. Range deliberately limited to < 4cm. 106/212/424 kbps. Three modes: Reader/Writer (reads passive tags), Peer-to-Peer (active device exchange), Card
Emulation (contactless payments, transit). EMV tokenisation in payments generates single-use card
numbers.
Relay attack proxies transaction over longer distance — NFC card in victim's pocket can be used at a payment terminal 100m away. Malicious NFC tag: Placed on a poster or public surface, triggers a URL, BT pairing request, or Wi-Fi credential change on any unlocked NFC-enabled phone that touches it.
Transit card investigation: A Delhi Metro NCMC card is reported stolen. What data does the card hold? Can it be cloned? (HF ISO 14443 with DES/3DES. partially vulnerable). How does forensic examination of NFC transaction logs establish when and where the card was used?

## Slide 38: WiMAX • Cellular Security (GSM→5G) • IrDA
WiMAX — IEEE 802.16
Metropolitan Area Network broadband. 802.16e: OFDMA, 75 Mbps, PKMv2 with X.509 certificate mutual authentication, AES-CCM data encryption. 802.16m: 1 Gbps. Range up to 50 km. Largely superseded by LTE/5G.
PKMv1 (legacy): one-way authentication only (BS authenticates to SS but NOT vice versa). Rogue base station attack possible. Management frames unauthenticated — DoS via forged frames.
Cellular Security — GSM to 5G
GSM (2G): A5/1 stream cipher — BROKEN. One-way authentication (phone authenticates to network, not vice versa). IMSI transmitted in plaintext → IMSI Catcher (Stingray) attack.
3G UMTS: Mutual authentication introduced (USIM challenge- response). KASUMI cipher (A5/3) — related-key attack found. Significantly stronger than 2G.
4G LTE: AES-EEA encryption, mutual auth, integrity-protected control plane. SS7 protocol exploitable for SMS interception. IMSI still obtainable at handover to 2G.
5G NR: SUCI (Subscriber Concealed Identifier) encrypts IMSI over air → blocks IMSI catchers. 256-bit ZUC/AES/SNOW3G ciphers. NSA mode falls back to 4G core.
IrDA / Infrared
Line-of-sight, < 1m range. Once common for device pairing. IrDA: no native encryption. Still used for TV remotes, industrial sensors, medical equipment. IR remote replay: capture IR codes, replay with any IR LED — controls any unencrypted IR device.

## Slide 39: Protocol Comparison Summary
Protocol | Frequency | Range | Encryption | Key Vulnerability
Wi-Fi 802.11 | 2.4/5/6 GHz | 30–300m | WPA3/AES | WEP broken; KRACK; deauth spoof
Bluetooth | 2.4 GHz | 1–100m | E0/AES-CCM | BlueBorne RCE; KNOB entropy=1bit
BLE | 2.4 GHz | 1–50m | AES-CCM (4.2+) | BLESA reconnect; eavesdropping
ZigBee | 2.4 GHz | 10–100m | AES-128 | Plaintext key join; default keys
Z-Wave | 868/908 MHz | 30–100m | AES-128 (S2) | S0 key=0x00; downgrade
RFID LF | 125 kHz | <10cm | None | Trivial cloning (Proxmark3)
NFC/RFID HF | 13.56 MHz | <4cm | Optional AES | Relay attack
GSM/2G | 850–1900 MHz | 1–35km | A5/1 (broken) | IMSI catcher; A5/1 cracked
5G NR | Sub- 6GHz/mmW | m–kms | AES-256/ZUC | NSA mode fallback

## Slide 40: Examination Preparation — Expected Question Types
DESCRIBE / EXPLAIN (8–10 MARKS)
insecure?
Describe the complete 802.11 MAC frame structure with all
fields and sizes
Explain the Frame Control field with a bit-level diagram
Explain the WEP encryption mechanism. Why is WEP
Describe the WPA2 4-way handshake message by message
with the PTK derivation formula
5. Explain KRACK. What is the mechanism? Which protocols are affected? How is it mitigated?
COMPARE / DISTINGUISH (5–8 MARKS)
1. Distinguish between promiscuous mode and monitor mode
with reference to wireless forensics
2. Compare WEP, WPA, WPA2, and WPA3 on: cipher, key
3. Compare WPA2-Personal and WPA2-E
management, known attacks, and statusnterprise. For which
use case is each appropriate?
4. Distinguish between Deauthentication and Disassociation
frames. What attack do they enable?
5. Compare ZigBee and Z-Wave for use in a smart building. Which is more secure and why?
APPLICATION / SCENARIO (10–15 MARKS)
1. Design a secure WLAN for a bank branch with 50
employees. Justify each control selected.
2. An attacker sits in a café car park with Kali Linux. Describe
what they capture passively in 10 minutes.
3. Your WIDS alerts on an unknown BSSID with the corporate
SSID. Describe the investigation and response steps.
4. A hospital uses ZigBee for medical equipment sensors.
Conduct a threat analysis and recommend countermeasures.
5. PMKID vs traditional 4-way handshake capture: which is
easier for the attacker and why?
SHORT ANSWER / FORMULAE (2–3 MARKS)
it contain?
What is the RSN IE? Where is it transmitted and what does
Write the PMKID formula. What information does an
attacker need to compute it?
3. What is SAE? How does it prevent the offline dictionary
attack that affects WPA2-PSK?
how?
What is 802.11w? What specific attack does it prevent and
What is the split-PIN design flaw in WPS? What is the
maximum number of attempts required?

## Slide 41: Wireless Network Security
U N I T I V
802.11 MAC frame: Frame Control (16 bits, bit-level), ToDS/FromDS (4 combinations), all management subtypes, Beacon RSN IE
WEP → WPA/TKIP → WPA2/AES-CCMP → WPA3/SAE: each generation patched the cryptographic flaws of its
predecessor
4-Way Handshake: PTK = PRF(PMK||ANonce||SNonce||AP-MAC||STA-MAC). KRACK = nonce reuse. PMKID = single EAPOL frame attack
Monitor mode (RFMON) for forensic capture — NOT promiscuous mode. Full 802.11 MAC headers, all SSIDs, all
management frames
Deauth flood → 802.11w fix. Evil Twin → WIDS detection. WPS PIN → disable entirely. Karma/MANA → MAC
randomisation does not help
Bluetooth: BlueBorne (airborne RCE) + KNOB (key entropy = 1 bit). ZigBee: plaintext key join. Z-Wave S0: key = 0x00 × 16
RFID LF: trivially cloneable with Flipper Zero. NFC: relay attack. GSM A5/1: broken. 5G: SUCI blocks IMSI catchers
Col Nidhish Bhatnagar (Retd.) | Professor of Practice | School of Cyber Security C Digital Forensics | NFSU Delhi Campus